## Slide 1
Wearable ECG Monitoring Device
Group Members
Dinusha Dissanayaka
Dulith Kavinda
Udara Deshan
Tharusha Nimesh
Senuda Ratnayake
Team Intelliave

## Slide 2
Problem Statement & Motivation
  Limited Monitoring Duration: Standard ECG systems record only 5–10 second snapshots, making it difficult to detect intermittent arrhythmias or long-term cardiac changes.
  Risk of Misdiagnosis: Atypical cardiac symptoms can be mistaken for less serious conditions, delaying timely treatment.
  High Clinician Workload: Manual ECG interpretation in busy emergency units increases workload, diagnosis time, and the risk of human error.
  Lack of Real-Time Intelligence: Most affordable portable ECG devices cannot simultaneously provide continuous monitoring and real-time anomaly detection
The Problem

## Slide 3
Proposed Solution: IntelliWave
IntelliWave is an affordable, ultra-portable, battery-powered 3-lead wearable ECG monitoring system designed for continuous cardiac monitoring of high-risk patients. It combines long-term ECG recording with an embedded explainable AI module that detects waveform anomalies in real time, providing intelligent decision support to reduce clinicians' workload and enable earlier diagnosis and intervention.

## Slide 4
Problem Validation
Would you find it valuable to have a tool that digitize ECGs and provides AI-based diagnostics?
solutions for this challangers
What challenges do you face in interpreting ECGs?

## Slide 5
Key Features
Real-time ECG monitoring with continuous heart rhythm tracking and instant alerts for abnormal patterns.
Seamless wireless connectivity via Bluetooth to mobile.
Ultra-compact and lightweight design.
Extended battery life of up to 24 hours on a single charge ensures uninterrupted monitoring and peace of mind.
We aim to keep the cost low while ensuring product quality.

## Slide 6
Product Specifications
Physical Specs :
Signal specs :
Power specs :
  Dimension : 75mm x 45mm x 26mm
  Weight : 70g
  Pocket friendly & Wearable design.
  Sample Rate : 250 SPS
  Notch Filter :50Hz (power line rejection, software)
  Baud Rate: 9600
  Supply Voltage : 3.3V regulated
  Rated current : Maximum 60mA, Typical 45mA.
  USB input charging : 5V, 500mA
  Battery : 3.7V 1200mAH LiPo Battery ( 24h Expected battery life)

## Slide 7
Connetivity:
  Bluetooth 4.0 (Low Energy)
  Band : 2.4GHz ISM band.
  Upto 10m in open space.
Indicators & UI
  Power status (Green)
  BLE connection status (Blue)
Mobile application:
  Platform : Android/IoS compatible software
  Display : Real time ECG waveform (Lead I, II, III)
  Heart Rate : Real time BPM display, Anomaly Notification.
  Recording : Manual trigger / auto 30 second recording
  Capability to send ECG reports to doctor, save ECG reports in PDF format.

## Slide 8
System Architecture
ECG Electrodes
Analog Front-end (AD8232)
MCU
(STM32F103C8T6)
Bluetooth Module
(HM-10)
Mobile
Application
Multi Level Calasification
Anomaly Detection
Displaying Real Time Anomaly
Notification

## Slide 9
PCB Design

## Slide 10
PCB Design - Layers

## Slide 11
Final Enclosure

## Slide 12
AI & Mobile Application

## Slide 13
Similar Products in the Market

## Slide 14
CNN Multi lable Classification Model

## Slide 15
Final product

## Slide 16
Mobile Application

## Slide 17
Cost Distribution - For the Project

## Slide 18
Volume Production Costing and Retail Price
Target Selling price : 30 000 LKR

## Slide 19
  B2C market : As a personal health check equipment.(For cardiac patients with high risk, personal health enthusiasts)
  B2B market : For hospitals to monitor patients continously outside home.(Where it need to monitor ECG for longer time (ex: 24h ECG)Expected Sales:
  Hardware sales (one time payment)
  SaaS model for Mobile application (Premium features ex: cloud storage)
  Subscription plan for hospitals.(As cloud storage charge)
Business Model for the Product

## Slide 20
Thank You