## Slide 1
IntelliWave
Wearable ECG Monitoring with Explainable AI for Early Detection of
Cardiac Anomalies in High-Risk Patients
PROBLEM
Rural clinics lack ECG access; short clinical snapshots miss intermittent arrhythmias, delaying life-saving care.
SOLUTION
A 3-lead wearable that logs continuous cardiac data and flags anomalies in real time via an on-device, explainable AI classifier.
IMPACT
Empowering continuous, non-invasive cardiac care by turning raw biopotential data into immediate, actionable clinical insights right at the edge.
3-Lead Wearable
AD8232 AFE · 200 g
Edge AI Triage
1D-ResNet · Macro F1 0.61
BLE Telemetry
250 Hz · HM-10 module
70.5 h Battery
600 mAh Li-Po
30%+
of premature deaths in
Sri Lanka linked to CVD
0.83
MI recall on the reduced
3-lead test set
30,000
LKR target retail price
(>80% gross margin)
IEC 60601-1 / 60601-2-47 · ANSI/AAMI EC38 · IEC 60601-1-2 EMC
Analog Front-End (AD8232) → STM32F103C8T6 MCU → HM-10 BLE → Mobile/Web App → Multi-Level AI Classification → Real-Time Anomaly Alert
EN2160 Electronic Design Realization · Department of Electronic & Telecommunication Engineering, University of Moratuwa
Dinusha · Dulith · Deshan · Dhananjaya · Senuda
Novel Innovation: We are democratizing cardiac care with a novel, low-cost, clinical-grade ECG signal that embeds machine learning directly on the device for real-time, continuous anomaly detection.